## Slide 1
PhD Student
AUDOUX Yohann yohann.audoux@ensam.eu
Supervisors
Pailhès Jérôme (I2M) jerome.pailhes@ensam.eu
Montemurro Marco (I2M) marco.montemurro@ensam.eu
Séminaire 01/10/18
ENS Rennes
Non-Uniform Rational B-Splines (NURBS) hypersurfaces for metamodeling
Notes: I2M
IMC
Le2i

## Slide 2
Design space
Metamodeling, what is it?
  A “model of the model”
  Learning / calibrating phase
Design variables : 10
Possible values : 7
Finite element computation : 10 minutes
Number of points : 282 billions
Computation time: 89 years
Domain of values
Design space
Design space:
Computer performance is often use to improve simulation complexity over computation time
Surrogate model, why?
  Improve computation time
  Use less memory space
Context and purposes
However, for optimization purpose, this simulations could be launch thousands of times
Séminaire 01 / 10 / 18
ENS Rennes

## Slide 3
Metamodeling
Current methods:
Data available:
Temperature field
Stress field
Displacement field…
Strain field
Learning or calibrating phase
Surrogate model
- T(x , y, z, var_1, …, var_n)
- σ(x , y, z, var_1, …, var_n)
- u(x , y, z, var_1, …, var_n)
- ξ(x , y, z, var_1, …, var_n) - …
Séminaire 01/10/18
ENS Rennes

## Slide 4
Metamodeling
Advantages:
  Accurate for non-linear problems
  Able to give multiple output
  Able to deal with thousands of inputs
Limitations:
  Multiple output is often less accurate
  “Black box”
  Only empiric rules for neural and layer number
  Trial-and-error
Current methods:
  Artificial Neural Network (ANN)
Séminaire 01/10/18
ENS Rennes

## Slide 5
Metamodeling
Advantages:
  Computational complexity scales linearly with the dimension n
  Can be utilized for direct computation (separable variables)
  A priori method
Limitations:
  Less accurate for non- linear problems
  Each output need its computation
  Design variables need to be separable
  For high number of variables, m could be very high
  Overfitting possible
  m is the number of “mode”
  It depends on the wanted accuracy
Current methods:
  Proper Generalized Decomposition (PGD)
Séminaire 01/10/18
ENS Rennes

## Slide 6
Metamodeling
Proposed method:
  Use surrogate models based on Non-Uniform Rational B-Splines (NURBS)
Advantages:
  Known in CAO for non-convex surface and curve fitting
  Multiple output
  Able to deal with non-linear problems
Limitations:
  Few literature is available for n-D NURBS surfaces
  Only iterative methods that focus on control points number
  High number of parameters (Knot vectors, control points position, …)
Séminaire 01/10/18
ENS Rennes

## Slide 7
: 2D or 3D vector of curve coordinates at parametric location u.
: the i-th Control Point (CP)
: the weight affected to the CP i
: the number of CPs
: the p-th degree B-Spline blending function recursively defined by
NURBS Framework
Curves
Function
Weight effect on a NURBS Curve
Séminaire 01/10/18
ENS Rennes

## Slide 8
NURBS Framework
Séminaire 01/10/18
ENS Rennes

## Slide 9
NURBS Framework
Hypersurfaces
Function
Surfaces
Function
Séminaire 01/10/18
ENS Rennes
Notes: Les fonctions de base ne sont calculées qu’une seule fois pour toutes les sorties

## Slide 10
Optimization problem formulation
Limitation:
Non convex problem when adding CP’s number, degrees and knot values as parameters
Advantages:
Objective is to minimize the number of data
Constraints threshold can be set according to the accuracy given by the mean to obtain the TPs
Stopping criteria can be linked to a wanted compression rate
Séminaire 01/10/18
ENS Rennes

## Slide 11
Parameters tuning the shape of a n-D NURBS hypersurface:
  The number of CPs along each direction
  The degree of the blending functions along each direction
  The internal knot vectors values along each direction
  The weight associated to each CPs
  The control points coordinates
Current literature:
  B-Spline instead of NURBS -> all weights are equal to 1 (B-splines) or set by the mean of empiric rules
  Degrees are fixed to 1 or 2
  Knot values are set by empiric rules
  Iterative procedure focused on finding the optimum number of control points
    Incrementing the number starting from few points (corner)
    Decreasing starting from a high number (interpolation)
Proposed approach -> Special GA (Montemurro, 2012) able to deal with design problems with a “variable number of design variables” to calculate automatically all the NURBS hypersurface parameters
Variable number of parameters
Numerical strategy
Séminaire 01/10/18
ENS Rennes

## Slide 12
Numerical strategy
Hybrid optimization tool:
Séminaire 01/10/18
ENS Rennes

## Slide 13
Numerical results
Benchmark case, displacement field over a pierced thin plate:
Design variables:
Thickness t
Radius r
Output of the model:
Displacement field
Data base generated by the mean of FEM code (ANSYS) on 21 different thickness and 21 different radius
Séminaire 01/10/18
ENS Rennes

## Slide 14
Numerical results
Displacement field at t and r fixed
Benchmark case, displacement field over a pierced thin plate:
Séminaire 01/10/18
ENS Rennes

## Slide 15
Numerical results
Variables |  | x | y | t | r | Number of points | Max error (%) | Mean error (%)
 |  | 151 | 31 | 21 | 21 | 2 064 321 |  | 
Iterative |  | 2 | 2 | 2 | 2 | 1 334 256 |  | 
 |  | 131 | 27 | 18 | 18 |  |  | 
Hybrid optimization (3 pop x 100 ind ) |  | 1 | 1 | 4 | 1 | 12 726 |  | 
 |  | 100 | 8 | 6 | 1 |  |  | 
Iterative |  | 2 | 2 | 2 | 2 | 811 512 |  | 
 |  | 116 | 23 | 16 | 16 |  |  | 
Hybrid optimization (3 pop x 200 ind ) |  | 1 | 1 | 4 | 1 | 2 736 |  | 
 |  | 11 | 18 | 5 | 1 |  |  | 
Variables |  | x | y | t | r | Number of points | Max error (%) | Mean error (%)
 |  | 151 | 31 | 21 | 21 | 2 064 321 |  | 
Iterative |  | 2 | 2 | 2 | 2 | 1 334 256 |  | 
 |  | 131 | 27 | 18 | 18 |  |  | 
Hybrid optimization (3 pop x 100 ind ) |  | 1 | 1 | 4 | 1 | 12 726 |  | 
 |  | 100 | 8 | 6 | 1 |  |  | 
Iterative |  | 2 | 2 | 2 | 2 | 811 512 |  | 
 |  | 116 | 23 | 16 | 16 |  |  | 
Hybrid optimization (3 pop x 200 ind ) |  | 1 | 1 | 4 | 1 | 2 736 |  | 
 |  | 11 | 18 | 5 | 1 |  |  | 
Benchmark case, displacement field over a pierced thin plate:
Séminaire 01/10/18
ENS Rennes

## Slide 16
Perspectives and conclusion
The proposed approach has shown better efficiency than existing iterative methods
Effect of the weights of the NURBS hypersurface
Use of the metamodel for optimization purpose
Computation with unsorted set of target points (FEM results on complex geometry)
Direct computation
Sampling method (ratio between wanted accuracy, data base generation time and surrogate model computation time)
Compare to other metamodeling methods
Séminaire 01/10/18
ENS Rennes

## Slide 17
Thanks for your attention !
Questions ?
Séminaire 01/10/18
ENS Rennes

## Slide 18
Genetic algorithm:
Numerical strategy
Séminaire 01/10/18
ENS Rennes

## Slide 19
Optimization problem formulation
Control points computation
B-Spline curves:
N- dimension B-Spline hypersurface:
175 GB
Séminaire 01/10/18
ENS Rennes

## Slide 20
Optimization problem formulation
NURBS Book algorithm extended to N-dimension:
Séminaire 01/10/18
ENS Rennes

## Slide 21
Optimization problem formulation
NURBS Book algorithm extended to N-dimension:
Fitting along the i-th dimension:
Séminaire 01/10/18
ENS Rennes

## Slide 22
Numerical results
Benchmark case, temperature field over a thin plate:
Design variables:
Thickness t
Convection coefficient h
Output of the model:
Temperature field
Data base generated by the mean of FEM code (ANSYS) on 21 different thickness and 21 different convection coefficient
Séminaire 01/10/18
ENS Rennes

## Slide 23
Numerical results
Benchmark case, temperature field over a thin plate:
Variables |  | x | y | t | h | Number of points | Max error (%) | Mean error (%)
 |  | 101 | 101 | 21 | 21 | 4 498 641 |  | 
Iterative |  | 2 | 2 | 2 | 2 | 2 424 168 |  | 
 |  | 86 | 85 | 17 | 17 |  |  | 
Hybrid optimization (2 pop x 120 ind ) |  | 4 | 1 | 3 | 4 | 12 480 |  | 
 |  | 51 | 4 | 5 | 7 |  |  | 
Hybrid optimization (10 pop x 100 ind) |  | 4 | 1 | 4 | 3 | 27 840 |  | 
 |  | 28 | 19 | 5 | 7 |  |  | 
Variables |  | x | y | t | h | Number of points | Max error (%) | Mean error (%)
 |  | 101 | 101 | 21 | 21 | 4 498 641 |  | 
Iterative |  | 2 | 2 | 2 | 2 | 2 424 168 |  | 
 |  | 86 | 85 | 17 | 17 |  |  | 
Hybrid optimization (2 pop x 120 ind ) |  | 4 | 1 | 3 | 4 | 12 480 |  | 
 |  | 51 | 4 | 5 | 7 |  |  | 
Hybrid optimization (10 pop x 100 ind) |  | 4 | 1 | 4 | 3 | 27 840 |  | 
 |  | 28 | 19 | 5 | 7 |  |  | 
Séminaire 01/10/18
ENS Rennes

## Slide 24
Numerical results
Benchmark case, temperature field over a thin plate:
Variables |  | x | y | t | h | Number of points | Max error (%) | Mean error (%)
Hybrid optimization (2 pop x 120 ind ) |  | 4 | 1 | 3 | 4 | 12 480 |  | 
 |  | 51 | 4 | 5 | 7 |  |  | 
Error on validation set (2 948 089 points) |  |  |  |  |  |  |  | 
Variables |  | x | y | t | h | Number of points | Max error (%) | Mean error (%)
Hybrid optimization (2 pop x 120 ind ) |  | 4 | 1 | 3 | 4 | 12 480 |  | 
 |  | 51 | 4 | 5 | 7 |  |  | 
Error on validation set (2 948 089 points) |  |  |  |  |  |  |  | 
Verification data base generated by the mean of FEM code (ANSYS) on 17 different thickness and 17 different convection coefficient (different from the first set)
Séminaire 01/10/18
ENS Rennes

## Slide 25
Numerical results
Benchmark case, displacement field over a pierced thin plate:
Design variables:
Thickness t
Force norm
Output of the model:
Displacement field
Data base generated by the mean of FEM code (ANSYS) on 21 different thickness and 21 different force norm values
Séminaire 01/10/18
ENS Rennes

## Slide 26
Numerical results
Benchmark case, displacement field over a thin plate:
Variables |  | x | y | t |  | Number of points | Max error (%) | Mean error (%)
 |  | 126 | 30 | 21 | 21 | 1 666 980 |  | 
Iterative |  | 2 | 2 | 2 | 2 | 1 062 423 |  | 
 |  | 108 | 26 | 18 | 18 |  |  | 
Hybrid optimization (3 pop x 100 ind ) |  | 4 | 4 | 1 | 1 | 43 500 |  | 
 |  | 28 | 24 | 14 | 3 |  |  | 
Variables |  | x | y | t |  | Number of points | Max error (%) | Mean error (%)
 |  | 126 | 30 | 21 | 21 | 1 666 980 |  | 
Iterative |  | 2 | 2 | 2 | 2 | 1 062 423 |  | 
 |  | 108 | 26 | 18 | 18 |  |  | 
Hybrid optimization (3 pop x 100 ind ) |  | 4 | 4 | 1 | 1 | 43 500 |  | 
 |  | 28 | 24 | 14 | 3 |  |  | 
Séminaire 01/10/18
ENS Rennes

## Slide 27
Numerical results
Approximation of the critical buckling load on an aeronautic stiffened panel :
Constant parameters [mm]:
Input of the model:
  : number of plies for skin and stringer respectively
  : first and second anisotropic moduli of the membrane stiffness matrix
Output of the model:
Critical buckling load
Séminaire 01/10/18
ENS Rennes

## Slide 28
Variables |  |  |  |  |  |  |  | Number of points | Max error (%) | Mean error (%)
 |  | 7 | 7 | 7 | 7 | 7 | 7 | 117 649 | / | /
Iterative |  | 2 | 2 | 2 | 2 | 2 | 2 | 117 649 |  | 
 |  | 6 | 6 | 6 | 6 | 6 | 6 |  |  | 
Gradient |  | 2 | 2 | 2 | 2 | 2 | 2 | 117 649 |  | 
 |  | 6 | 6 | 6 | 6 | 6 | 6 |  |  | 
Hybrid |  | 1 | 1 | 6 | 6 | 2 | 2 | 28 812 |  | 
 |  | 2 | 3 | 6 | 6 | 6 | 6 |  |  | 
Variables |  |  |  |  |  |  |  | Number of points | Max error (%) | Mean error (%)
 |  | 7 | 7 | 7 | 7 | 7 | 7 | 117 649 | / | /
Iterative |  | 2 | 2 | 2 | 2 | 2 | 2 | 117 649 |  | 
 |  | 6 | 6 | 6 | 6 | 6 | 6 |  |  | 
Gradient |  | 2 | 2 | 2 | 2 | 2 | 2 | 117 649 |  | 
 |  | 6 | 6 | 6 | 6 | 6 | 6 |  |  | 
Hybrid |  | 1 | 1 | 6 | 6 | 2 | 2 | 28 812 |  | 
 |  | 2 | 3 | 6 | 6 | 6 | 6 |  |  | 
Numerical results
Approximation of the critical buckling load on an aeronautic stiffened panel :
Séminaire 01/10/18
ENS Rennes